Note that this specification only covers the communication between the PC and the Host Controller

Data Encoding Determinations

Type	Datatype	Encoding	Range	Resolution
Device ID	Unsigned 3 Bit	See section below	0 – 7	1
IO Pin number	Unsigned 8 Bit		0 – 255	1
IO Pin mode	Unsigned 4 Bit	Join value of multiple pins for transmission	0 – 15	1
IO Pin value	Boolean	Join value of 8 pins for transmission if sensible	0 – 1	1
Analog Pin value	Unsigned 8 Bit	value = V * 256/Vmax <=> V = Vmax/256 * value; Absolut	0 – Vmax(5V)	~20mV
Encoder value	Signed 16 Bit	Number of counts; Relative	-32768 – 32767	1
PWM frequency	Unsigned 12 Bit	f = value*16 <=> value = f/16	0 – 4095	16
PWM dutycycle	Signed 12 Bit	2048 ≙ 100%, 1 ≙ 0.05%; Absolut; Join frequency and dutycycle in 3 bytes	-2048 – 2047	1

Relative values are the difference related to the value returned by the last read, i.e. always return the difference between two reads

DeviceId

The deviceId is used for identication of the slaves as all use the same UART bus. Upon identification, each slave messages its programmed Id and its capablilities. DeviceId 0 is reserved; in communication between PC and Host, the Host uses deviceId 0 for its own capablilities.

List of Opcodes

Name	Decimal	Binary	Decription	Index (nnn)	Additional Message	Response
RESET	0	0b00000000	Send this message 20 times to reset Host and all Slaves	-	none	reset
ALIVE	1	0b00000001	Keep-alive message	-	none	none
UPCAP	2	0b00000010	Capabilities have changed (Host->PC)	-	none	none
	3….7	0b00000011..0b00000111	reserved
SLVDSC	8...15	0b00001nnn	Message slave disconnected (Host->PC)	deviceId	none	none
SLVCON	16...23	0b00010nnn	Message slave connected (Host->PC)	deviceId	none	none
SETUP	24...31	0b00011nnn	Set IO, Encoder and PWM modes (PC->Host)	deviceId	Modes of each instance	none or Error
STIO	32...39	0b00100nnn	Set output values (PC->Host)	deviceId	Values of each out-pin	none
STPWM	40...47	0b00101nnn	Set PWM parameters (PC->Host)	deviceId	PWM parameters	none
STALL	48...55	0b00110nnn	Set all out and PWM values in single message (PC->Host)	deviceId	outpin and PWM values	none
RQCAP	56...63	0b00111nnn	Request capabilities of device (PC->Host)	deviceId	none	GTCAP
GTCAP	64...71	0b01000nnn	Get capabilities of device (Host->PC)	deviceId	Capabilities	none
GTIO	72...79	0b01001nnn	Get input values (Host->PC)	deviceId	IO values of each pin	none
GTENC	80...87	0b01010nnn	Get encoder values (Host->PC); Relative values	deviceId	Change of each encoder	none
GTVLT	88...95	0b01011nnn	Get analog voltages (Host->PC)	deviceId	Values of all analog pins	none
GTALL	96...103	0b01100nnn	Get all input, encoder and output values (Host->PC)	deviceId	All values	none
	104..223	0b01101000..0b11011111	reserved
ERROR	224..255	0b111nnnnn	Error with code nnnnn detected	Error code	none	none

1. Messages with direction noted, can only be issued in this direction. If the message is received unexpectedly, it is ignored
2. Reserved opcodes must not be used and are ignored by the receiver
Opcode-only messages

Offsets	Octet	0					1					2					3
Octet	Bit	0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19	20	21	22	23	24	25	26	27	28	29	30	31
0	0	Opcode					-

Use this message format for all opcodes which define no additional message bytes

SETUP messages

Offsets	Octet	0					1					2					3
Octet	Bit	0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19	20	21	22	23	24	25	26	27	28	29	30	31
0	0	Opcode					IO Message length					IO0 Mode				IO1 Mode				IO3 Mode				IO4 Mode ...
x	x	Encoder Message length					Encoder0 Mode				Encoder1 Mode				PWM Message length					PWM0 Mode				PWM1 Mode
x	x	... PWM Message (variable length)

This opcode is used to set the IO, PWM and Encoder modes. The analog measurement is enabled by setting pin mode to Analog.
If the number of channels/IOs is odd, leave the last nibble empty (0s). It will be ignored by the receiver.

IO Message length:
The length of the following message in bytes. This corresponds to pin number as pins = bytes * 2

IO Message:
Variable sized message where each nibble (4 bit) represents the mode of the corresponding IO. The maximum length is 255 bytes

Encoder Message length:
The length of the following message in bytes. This corresponds to encoder number as enc = bytes * 2

Encoder Message:
Variable sized message where each nibble (4 bit) represent the mode of the corresponding Encoder. The maximum length is 255 bytes

PWM Message length:
The length of the following message in bytes. This corresponds to PWM number as pwm = bytes * 2

PWM Message:
Variable sized message where each nibble (4 bit) represent the mode of the corresponding PWM peripheral. The maximum length is 255 bytes

STIO, GTIO messages

Offsets	Octet	0					1					2					3
Octet	Bit	0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19	20	21	22	23	24	25	26	27	28	29	30	31
0	0	Opcode					Message length					Message (variable legth) ...
x	x	... Message (variable length)

Message length:
The length of the following message in bytes. This corresponds to pin number as pins = bits = bytes * 8

Message:
Variable sized message where each bit represents the value of the corresponding IO. The maximum length is 255 bytes

STPWM messages

Offsets	Octet	0					1					2					3
Octet	Bit	0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19	20	21	22	23	24	25	26	27	28	29	30	31
0	0	Opcode					Message length					PWM0 Frequency					PWM0 Dutycycle
4	32	PWM0 Dutycycle					PWM1 Frequency					PWM1 Dutycycle
x	x	... Message (variable length)

Message length:
The length of the following message in bytes. This corresponds to PWM number as pwm = bytes / 3

Message:
Variable sized message where each 3 bytes represent the parameters of the corresponding PWM peripheral. The maximum length is 255 bytes

STALL messages

Offsets	Octet	0					1					2					3
Octet	Bit	0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19	20	21	22	23	24	25	26	27	28	29	30	31
0	0	Opcode					IO Message length					IO Message (variable length)
x	x	PWM Message length					PWM0 Frequency					PWM0 Dutycycle
x	x	... PWM Message (variable length)

Use this opcode as replacement for sending STIO and STPWM messages seperately. The result is equivalent

IO Message length:
The length of the following message in bytes (See STIO messages)

IO Message:
Variable sized message where each bit represents the value of the corresponding IO. The maximum length is 255 bytes

PWM Message length:
The length of the following message in bytes (See STPWM messages)

PWM Message:
Variable sized message where each 3 bytes represent the parameters of the corresponding PWM peripheral. The maximum length is 255 bytes

GTENC messages

Offsets	Octet	0					1					2					3
Octet	Bit	0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19	20	21	22	23	24	25	26	27	28	29	30	31
0	0	Opcode					Message length					Encoder0 value
4	32	Encoder1 value					Encoder2 value
x	x	... Message (variable length)

Message length:
The length of the following message in bytes. This corresponds to Encoder number as enc = bytes / 2

Message:
Variable sized message where each 2 bytes represent the value of the corresponding Encoder (difference since last read). The maximum length is 255 bytes
GTVLT messages

Offsets	Octet	0					1					2					3
Octet	Bit	0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19	20	21	22	23	24	25	26	27	28	29	30	31
0	0	Opcode					Message length					Analog0 value					Analog1 value
x	x	... Message (variable length)

Message length:
The length of the following message in bytes. This corresponds to Analog channels as adc = bytes

Message:
Variable sized message where each byte represent the voltage of the corresponding Analog input. The maximum length is 255 bytes

GTALL messages

Offsets	Octet	0					1					2					3
Octet	Bit	0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19	20	21	22	23	24	25	26	27	28	29	30	31
0	0	Opcode					IO Message length					IO Message (variable length)
x	x	Encoder Message length					Encoder0 value					Encoder1 value
x	x	Encoder1 value					Encoder2 value ...					Analog Message length
x	x	Analog0 value					Analog1 value					Analog2 value					Analog3 value
x	x	... Analog Message (variable length)

Use this opcode as replacement for sending GTIO, GTENC and GTVLT messages seperately. The result is equivalent

IO Message length:
The length of the following message in bytes (See GTIO messages)

IO Message:
Variable sized message where each bit represents the value of the corresponding IO. The maximum length is 255 bytes

Encoder Message length:
The length of the following message in bytes (See GTENC messages)

Encoder Message:
Variable sized message where each 2 bytes represent the value of the corresponding Encoder (difference since last read). The maximum length is 255 bytes

Analog Message length:
The length of the following message in bytes (See GTVLT messages)

Analog Message:
Variable sized message where each byte represent the voltage of the corresponding Analog input. The maximum length is 255 bytes

GTCAP messages

Offsets	Octet	0					1					2					3
Octet	Bit	0	1	2	3	4	5	6	7	8	9	10	11	12	13	14	15	16	17	18	19	20	21	22	23	24	25	26	27	28	29	30	31
0	0	Opcode					Encoder Count					PWM Count					IO Count
4	32	IO0 abilities				IO1 abilities				IO2 abilities				IO3 abilities				IO4 abilities				IO5 abilities				IO6 abilities				IO7 abilities
x	x	... IOx abilities (variable length)

This message is the response to a RQCAP message. The deviceId is the same as for the request.
If the deviceId is unknown to the Host, the Count fields are all 0 and no Message bytes are sent

Encoder Count:
The number of supported Encoder instances

PWM Count:
The number of supported PWM instances

IO Count:
The number of IOs in device

IO abilities:
Variable sized message where each nibble (4 bits) represents the abilities of the corresponding IO Pin. Each bit represents an ability of io_mode_t.
The maximum length is 255 bytes
Initialization routine

1. Powerup Host and Slaves. The Host will collect capabilities and deviceIds from each slave
2. PC sends RQCAP for each deviceId. The Host answers with the collected capabilities (GTCAP)
3. PC creates the neccessery pins in LinuxCNC HAL
4. PC sends SETUP for each deviceId after IO modes set in HAL
  – Normal operation starting here –
5. PC sends STPWM to set PWM frequency and dutycycle
6. PC sends STIO to set output values
7. PC may also use STALL for that
8. Host sends GTIO to notify PC about changed input values
9. Host sends GTENC to notify PC about changed encoder position
10. Host sends GTVLT to notify PC about changed analog value
11. Host may also use GTALL for that
12. Host sends ALIVE to PC if no other messages were exchanged in the last 500ms
  – Error cases –
13. The Host did not send any message in the last 500ms → Host is probably disconnected; Initiate E-Stop or warning
14. The Host sends SLVDSC if it received not message from a slave in the last 500ms → Slave probably disconnected; Initiate E-Stop or warning
15. The Host sends UPCAP if capabilities changed; Issue RQCAP and check for relevant changes
16. To recover from error cases, execute software reset by issuing RESET at least 20 times in a row